## Slide 1: Modul - Internet of Things (IoT) - 02-Vorlesung
Prof. Dr. Marcel Tilly
Fakultät Informatik, Cloud Computing

## Slide 2: Überblick
21. März Einführung in das Internet der Dinge
28. März IoT Architekturen
4. April Things und Sensoren
11. April From Device to Cloud
18. April Vorlesungsfrei – Ostern
25. April IoT Analytics
02. Mai Big Data in IoT
9. Mai Data Exploration
16. Mai IoT Platformen
23. Mai Entwicklung einer IoT Lösung
30. Mai Vorlesungsfrei; Christi Himmelfahrt
05. Juni opt. Gastvortrag – Digitalisierung
13. Juni Data Science in IoT
20. Juni Vorlesungsfrei – Fronleichnam
27. Juni Intelligente Cloud und intelligente Edge
04. Juli PStA Abschlusspraesentationen
PStA

## Slide 3: Sensor devices are becoming widely available
- Programmable devices
- Off-the-shelf gadgets/tools

## Slide 4: More Things
Home/daily-life devices
Business and
Public infrastructure
Health-care
…

## Slide 5: Things
Challenges
Memory
Processor
Energy (Battery) , lifetime
Security
Various generations (old vs new)
Heterogeneous platforms
Provisioning
Variety of device categories (sensor, gateways)
Variety of device types
Programming languages
Physical size
Inputs
Connectivity
Technology
Microcontroller vs OS powered
C, Java, Python, JavaScript, C++, C#, ….

## Slide 6: Initial thoughts about ‘Things’
We can turn almost every object into a “thing”.
A “thing” still looks much like an embedded system currently.
A “thing” generally consists of four main parts:
  Sensors & actuators
  (Micro) - Controller
  Communication unit
  Power supply
To be discussed:
A “thing” has the following properties:
  It’s generally powered by battery: This implies limited source of energy.
  It’s generally small in size and low in cost: This limits their computing capability.
  It doesn’t usually perform complicated tasks.
Power consumption is the main design issue.

## Slide 7: ‚Thing‘ Setup
Sensor(s)
Actor(s)
IO
ADC
Power unit
Communication
Controller
Memory
RAM
Flash
Memory
Processor
Energy (Battery) , lifetime
Security
-> Various generations (old vs new)
Heterogeneous platforms
-> Provisioning
-> Variety of device categories (sensor, gateways)
-> Variety of device types
Programming languages
Physical size
Inputs
Connectivity
ADC = Analog-to-digital converter

## Slide 8: ‚Thing‘ Setup
A ‘thing’ consists of several components
  Controller: Central processing unit (CPU)
  Memory for application and data
    Usually different memory types are used for application and data
  Communication interface
    Wireless radio interface with antenna
    Wired
  Sensors/Actors
    Interface to the real world
    Monitoring, changing of real world phenomena
  Power unit
    Power supply for all the components

## Slide 9: Controller
Four important factors for the controller
  Number of transistors -> size, cost, power
  Number of clock cycles -> power
  Time to develop -> cost, acceptance
  Nonrecurring engineering cost (NRE) -> cost, acceptance
Ideal: Minimize all factors at the same time!

## Slide 10: Controller Types
The controller is the Central Processing Unit (CPU) of the device
Different architectures possible
  Microcontroller (MCU)
    Resource constrained compared to desktop processors
    Software controlled, general purpose
  Digital Signal Processor (DSP)
    Processing of large data streams, parallelizing
    Hard-wire basic functions
  Field-Programmable Gate Arrays (FPGA)
    Special hardware, expensive
    Limit coding to configuration
  Application-Specific Integrated Circuits (ASIC)
    Special hardware designed only for one application
    Possibly embedding several MCU or DSP cores
  General purpose CPU
    Resource consuming but flexible
    Software controlled

## Slide 11: Controller
 | Time to Market | Perfor-mance | Price | Develop-ment Ease | Power | Features Flexibility
MCU | Excellent | Fair | Excellent | Good | Fair | Excellent
DSP | Excellent | Excellent | Good | Excellent | Excellent | Excellent
FPGA | Good | Excellent | Poor | Excellent | Poor | Good
ASIC | Poor | Excellent | Excellent | Fair | Good | Poor
CPU | Excellent | Excellent | Good | Excellent | Poor | Excellent

## Slide 12: Overview of some MCUs

## Slide 13: Memory
Properties
  Often different program and data memory
  No memory management unit (MMU) available
  Size of memory varies
    May depend on the application
Types of memory
  Random Access Memory (RAM)
    Store temporarily sensor data and messages
  Electrically Erasable Programmable Read-Only Memory (EEPROM)
    Stores the program code
    Operates on bytes
  FLASH Memory
    Non-volatile memory
    Stores the program code
    Stores data if RAM too small or protection against power loss required
    Operates on blocks (read, write)
    High delay and energy consumption

## Slide 14: Communication interface
Communication interface is required to exchange data with other devices
Typical communication media
  Radio
    Bluetooth, ZigBee, WiFi, LORA, …
  Infrared (IR)
    Directed / undirected
  Ultrasonic
    More in military applications
  Sound
    Underwater communication
Communication interface has high energy consumption
  Radio interface consumes the most energy usually

## Slide 15: Platforms Overview

## Slide 16: Platforms: IRIS Motes
Processor
  XM2110CA based on Atmel ATmega1281
  8 bit Microcontroller
  8 MHz
  Compute power similar to 8088 CPU from the original IBM PC (~1982), but reduced energy consumption
Radio chip
  AT86RF230
  IEEE 802.15.4
  ZigBee compatible
  2.4 GHz, 250 kbps, up to 300 m (outdoor), up to 50 m (indoor)
Memory
  4 kB EEPROM
  8 kB RAM
  128 kB program Flash Memory
  512 kB measurement Flash Memory

## Slide 17: Plattform: Freedom Development Boards
Processor
  MK22FN512VLH12 MCU
  120 MHz
  512 KB flash memory
  128 KB RAM
  low-power, and crystal-less USB in 64 LQFP package
Radio
  Optional header for add-on RF module: nRF24L01+ Nordic 2.4 GHz radio
  Optional header for add-on Bluetooth module: JY-MCU BT board V1.05 BT

## Slide 18: Plattform: Arduino Uno
Processor
  Microchip ATmega328P
  SRAM: 2 KB
  EEPROM: 1 KB
  Clock Speed: 16 MHz
  Flash Memory: 32 KB of which 0.5 KB used by bootloader
Radio
  No Radio default but everything is available as breakouts

## Slide 19: Sensors available in Market

## Slide 20: Plattform: Raspberry Pi

## Slide 21: Plattform: Beagle Bone
Processor
  AM335x 1GHz ARM® Cortex-A8
  512MB DDR3 RAM
  4GB 8-bit eMMC on-board flash storage
  3D graphics accelerator
  NEON floating-point accelerator
  2x PRU 32-bit microcontrollers
Connectivity
  USB client for power & communications
  USB host
  Ethernet
  HDMI
  2x 46 pin headers
Software
  Debian
  Android
  Ubuntu

## Slide 22: Plattform: Intel Galileo
Processor
  1 Core 32-bit Intel Pentium processor-compatible ISA Intel Quark SoC X1000
  400 MHz
  16 KB L1 Cache
  512 KB SRAM
  Integrated real-time clock (RTC)
Storage
  8 MB NOR Flash for firmware and bootloader
  256 MB DDR3; 800 MT/s
  SD card, up to 32 GB
  8 KB EEPROM
Connectivity
  USB 2.0
  RJ45 Ethernet
  10-pin JTAG for debugging
  6-pin UART
  6-pin ICSP
  1 mini-PCI Express slot
  1 SDI

## Slide 23: Plattform: Tessel
Procesor
  580MHz Mediatek MT7620n
  48MHz Atmel SAMD21 coprocessor
  64 MB DDR2 RAM & 32 MB Flash
  Plenty of space for your code
Connectivity
  802.11 b/g/n Wi-Fi
  Ethernet
Programming Language
  JavaScript

## Slide 24
Some Project Ideas